- PLACING THE HOIST IN SERVICE

  - CONNECTION TO THE MAINS SUPPLY

Please check whether the voltage stamped on the data plate corresponds to that of the  mains supply.  The wiring diagram contained in this book gives the necessary information for connecting the electrical hoist to the mains supply.

  - EARTHING CONDUCTOR

The earthing conductor marked green / yellow in the supply line must be connected to the earth terminal.

  - CHECKING THE PHASE CONNECTIONS

When the push-button on the pendant control station is pressed for lifting, the load must rise.  If it goes down, switch off the current supply and reverse two phases on the supply.  Note that hoist was left with about one diameter turn before cutting the top limit for this purpose.

  - FINAL SETTING OF LIMIT SWITCH

After checking the earth conductor, mains supply and phase connections, the hook should be brought to the top position until the limit switch stops the hoisting movement.  Correct adjustment of the switch is important before a hoist is put into service as accidents may occur otherwise.  The limits in the limit switch enclosure are adjusted to operate in accordance with the longest possible hook travel.  The limits must be readjusted to suit the local requirements.

  - START-UP CHECK AND LUBRICATION

    - If supply, erection and commissioning are

done by Condra, all lubricant points will be adequately greased and the gearbox assembly filled with oil.  The rope and rope drum are lubricated with special grease.

1.5.2	When crane components and individual hoists are supplied, please refer to our maintenance check and lubricant specifications contained in this book.

  - CLEARANCE CHECK

Check all end positions of the hoist or crane for possible obstructions in the crane and hoist operating area.

  - LOAD TEST

A load test is required.

  - EARTH LEAKAGE TEST

After extended periods of storage or stoppage, an earth leakage test is required to check for ingress of moisture.

- GENERAL DESCRIPTION

  - HOIST BRAKE ASSEMBLY

The brake is a direct current brake consisting of a rectifier, a DC magnet, single or double brake discs and linings mounted on a spline.  This arrangement eliminates any axial pressure on the motor bearing.  As the motor is energized, the DC magnet is activated and the pressure plate is pulled against the springs, thus releasing the brake.  The brake is applied by multiple springs when the magnet is de-energized.  As the brake is electrically connected with the motor circuit, it is switched with the motor; thus in the event of power failure, the brake engages automatically (fail to safety).

  - HOIST MOTOR

The hoist motor is a standard frame size, three-phase squirrel-cage induction motor with a special hoisting duty winding.  The totally enclosed fan-cooled motor employs Class ‘B’ or ‘F’ insulation.  The motor is fully insulated and can withstand high temperatures.  The starting torque is more than 200% of the normal torque.  The normal rating is 180 starts per hour; 40% ED.

  - HOIST GEARS

All gears are made of high-quality steel and designed for oil bath lubrication in a totally enclosed gearbox.  Provision has been made for long service life.

  - HOIST ROPE, DRUM AND ROPE GUIDE

ASSEMBLY

The rope is of the normal right-hand lay with a fibre core, a 6 x 36 construction.  For lifts in excess of 10 m, a non-spin rope with a steel core and a 7 x 36 construction is to be used.  The rope drum is manufactured from mild steel with machined grooves taking the total length of rope.  The standard drum diameter is approximately 19 times the diameter of the rope.  The rope guide is a solid, cast bronze ring, precision-machined to suit the drum

grooves.  It can be removed from the end of the drum and refitted.

2.5	BOTTOM BLOCK

The cast-iron rope sheaves have a minimum diameter of 20 times larger than the wire rope diameter and are fitted with anti-friction bearings.  The stamp forged annealed steel hook is tested to 200% of the safe working load and is mounted with a thrust bearing, enabling it to revolve with the load.

2.6	ROPE PULLEYS

All the pulleys in the bottom and top blocks are fitted with sealed ball-bearings and are lubricated for life.

  - LIMIT SWITCH AND GUIDE TUBE

ASSEMBLY

A limit switch is mounted in the hoist in order to limit the hoisting and lowering motion.  The switch, of the self-resetting type, automatically cuts out the hoisting motor after the rope guide has reached its end position on the rope drum.  It offers protection against inadvertent operation of the hoist.  The limit switch also activates in case of phase reversal, thus preventing damage to the hoist when phase rotation is changed accidentally.  In case of a phase reversal, the limit switch is activated and neither the hoisting or lowering modes can be operated.

We advise that a technician be called in from our nearest branch to repair or replace the service limit switch.

The collars are adjusted only if the rope is changed.

  - CROSS-TRAVEL AND LONG-TRAVEL DRIVE UNITS AND BRAKE

The brake is a direct current disc brake, consisting of a rectifier, a DC magnet, single

brake disc pressure plate and brake spline.  The brake linings are renewable.  The brake is spring-applied and magnetically released by means of the DC magnet.  As the brake is mechanically and electrically connected to the motor, it is switched with the motor.  Thus, in the event of a power failure, the brake engages automatically (fail to safety).

  - HOIST ASSEMBLY

All hoist operations are controlled by push-button switches on the pendant control.  All

controls are effected through magnetic contactors and an auxiliary circuit for positive

reliability.  An electromagnetic brake retains

the load safety in case of emergency or when

the power supply is switched off.  A limit switch stops overwinding and overlowering. 110 (volts) is used for the control circuits, unless otherwise requested.  All components of the hoist are unitized, simplifying dismantling and re-assembly during maintenance.

- MAINTENANCE INSTRUCTIONS

3.1.1	SERVICE INTERVALS

3.1.2	For class 1 am duty (normal workshop duty up to a maximum of 4 hours per day, under the load spectrum of 1) the cranes and / or hoists should be serviced / inspected every two months.

3.1.3	For class 3m duty (up to a maximum of 16 hours per day, under the load spectrum of 1) cranes and / or hoists should be serviced /inspected every month.

NOTE 1.	These intervals do not apply to cranes and hoists placed in special conditions such as foundries (over furnaces) or chemical plants, etc.  Advice on service intervals for cranes and hoists used in these conditions should be obtained from our service department.

2.	Please note also that whenever the hoist is used to install heavy machinery in new buildings, this cannot be regarded as normal working conditions and a shorter interval between services / inspections should be considered.

3.2 	SAFETY WARNINGS

    - Always make certain that the power supply to

the crane or hoist is switched off and the isolating switch is locked.  A warning note must be attached to the switch to guard against the power supply being switched on while maintenance work is in progress.

    - Check that all tools and/or equipment used

during erection, installation or service and repair have been removed from the crane / hoist before operating it.

  - SAFETY PRECAUTIONS

    - Maintenance work on the crane, hoist and

crawl must not start before the load has been removed and the power supply to the crane, hoist and crawl has been switched off.

    - For the maintenance and operation of all

equipment, all relevant official regulations and accident prevention regulation must be adhered to.

    - Tests and checks must be carried out as listed

in the check-list and also as stated in our Lubrication Schedule.

  - HOIST BRAKE ASSEMBLY

    - Adjustment for Lining wear

The wear on the brake linings has to be checked regularly in accordance with the instructions that follow and at the intervals specified in paragraph 3.1.  The lining wear is checked between the magnet and the pressure plate after the cover has been removed.  When new, the gap is adjusted to 0,6 mm for single discs and 0,8 mm for double discs.  Allowance has been made for a maximum gap of 1,6 mm, after which the load will induce progressive slipping of the linings.

    - Readjustment of brakes

If the wear on the brake has reduced the brake lining to 5 mm, renew the linings (refer to paragraph 3.4.3).  Check the distance between the pressure plates as follows:

- Remove the cover by removing the four screws.

- Loosen the locknuts on the three adjusting screws.

- Using a feeler guage, adjust the gap as specified (0,6mmfor single discs and 0,8mm for double discs).

- Insert the feeler guage between the magnet and the pressure plate as shown in Figure 1.

- Use the feeler gauge to ensure that the gap is uniform all the way around.

- Re-lock the adjusting screws by fastening the lock-nuts.

- Re-check the gap after re-locking the adjusting screws and readjust if necessary.

- Replace the cover and fasten the four screws.

    - Renewal of lining

- Remove the brake cover.

- Remove the fan by removing the tension pin or circlip.

- Loosen the lock-nuts on all three adjusting screws and remove the bolts.

- Remove the disc(s) and linings.

- Check the brake discs for distortion and wear.  The discs should be parallel within +- 0.02 mm.

IMPORTANT

Both the brake disc(s) and pressure plate must move freely on the spline and guide pins.

Recheck the brake adjustment after 2 hours of continuous operation.

    - Weather covers (where applicable)

Weather covers, where applicable, must be replaced as soon as possible to prevent damage due to rain or water.

    - Brake rectifier protection fuses

Only ‘ultra rapid’ type fuses should be used.  Contact Condra Service Department for information and/or the supply of spare fuses.  Do not run open circuit.

    - Replacement of hoist brake coil

- Follow the procedure set out in paragraph 3.4.3. a. – d.

- Disconnect the power supply to the DC magnet in the motor connection box.

- Remove the four nuts holding the magnet and the motor.

- Lightly tap against the back of the magnet to release the tight fit of the spigot.

- The magnet can now be pulled off without removing the pinion.

    - Replacement of hoist stator

- Switch off the main power supply.

- Disconnect the wires supplying the motor and brake magnet.

- Remove the fan cover.

- Remove the brake fan.

- Remove the brake plates and linings.

- Remove the nuts and spring washers from the motor studs.

- Remove the brake magnet and studs.

- Remove the stator, taking care not to touch the rotor and shaft.

- Fit the new stator, again taking care not to touch the rotor and shaft.

- Refit the brake magnet (NOTE: The brake cable side to be the same as the motor connections).

- Refit the nuts and spring-washers to the motor studs.  Tighten evenly all round.

- Refit the brake plates and linings (do not forget the springs).

- Reset the brake gap.

- Refit the brake fan.

- Reconnect the brake magnet and motor connections.

- Switch on the mains and carefully check the direction of the motor.  If the direction is incorrect, change the two phases.  Note that for two-speed motors the winding with higher resistance belongs to the slow speed.

While checking the motor direction, check that the brake plates and linings move freely.

- Refit the brake fan cover.  Retest the motor.

NOTE:  When the hoist motor is removed it is possible that the hoist rope will unwind down to the limit switch bottom position.  This will put the switch in the off position.  In this event, bridge out switch to activate the motor.  Remember to remove the bridge immediately after use.

  - DRUM, COVER AND ROPE GUIDE ASSEMBLY

    - Rope and rope guide

Regular greasing will increase the life of the rope and the rope guide.  Use graphite grease only.  Rope dressing must not be used.  In very dusty and gritty environments, the rope drum and rope guide should be cleaned thoroughly to remove all dirt before new graphite grease is applied.

    - Replacement of wire rope

The wire rope must be replaced if there is any sign of wear, tear, broken strands, corrosion or

permanent deformation such as kinks, bends, bruises, etc.

    - Removal of wire rope

- Lower the bottom block as far as the limit switch allows.

- Move the limit switch striker collar to the outermost position and operate the hoist in lowering mode until the drum nut is within 10mm of the rope clamps.

- Ensure that the correct reeving method is noted before removing the existing rope.  This will avoid confusion when fitting the new rope.

- Undo the rope clamps on the drum and on the fixed point.

- Unreeve the rope from the top and bottom blocks.

    - Fitting of new wire rope

This procedure should be carried out by experienced personnel only.

- Lay the total length of rope on the floor to eliminate twist.

- Feed the rope into the drum and tighten the rope clamp on the drum.

- Rotate the drum in lifting mode until the grooves of the rope are wound onto the drum.

- Lower enough rope to allow reeving of the top and bottom blocks.  Drive the bottom blocks into the top limit and fix the end of the rope so that a clearance of about a sheave diameter remains between the bottom block and the drum.

- Secure the loose end of the rope to the rope anchor.

- Set the lower limit switch striker.

  - LIMIT SWITCH

Correct adjustment of the switch is important, as accidents may occur otherwise.  Please consult the limit switch adjustment instructions.  The limit switch must be adjusted to suit the local requirements.

  - CROSS-TRAVEL AND LONG-TRAVEL DRIVE UNITS AND BRAKE

    - Adjustment of lining wear

The wear on the brake linings has to be checked periodically in accordance with the following instructions and at intervals specified in the maintenance instructions.  The wear can be checked between the magnet and the pressure plate.  When new, the gap is adjusted to 0,5mm and allowance has been made for a maximum cap of 1,5mm.

To adjust the brake, loosen the Allen-head cap screws and remove one shim from each of the three screws.  Tighten the screws again and check the gap by means of a feeler gauge.  If the wear on the brake has reduced the thickness of the brake lining to 5mm, renew the lining.

    - Renewal of lining

- Remove all three Allen-head cap screws.

- Remove the brake magnet, together with the pressure plate.

- Slide the brake lining off the centre spline.

- For re-assembly with the new brake lining, follow the reverse order of the above steps.

- Ensure that all the spacers and shims are fitted to give an equal gap of 0,5mm.  The brake will not operate otherwise.

    - Weather covers (where applicable)

Weather covers, where applicable, must be replaced as soon as possible to prevent damage due to rain or water.

    - Brake rectifier protection fuses

Only ‘ultra rapid’ type fuses should be used.  Contact Condra Service Department for information and/or the supply of spare fuses.

    - Replacement of coil

The operation is carried out in the same manner as the renewal of the lining.

- AFTER SALES SERVICE DIVISION

  - CRANE AND HOISTS SERVICES & INSPECTION REPAIRS AND LOAD TESTS AS PER OHA ACT (85/1993)

Condra (Pty) Ltd has an After Sales Service Division to cater for all your Crane and Hoist requirements after commissioning.  A 24 hour service is provided to contracted clients and

we recommend this approach to all of our clients.  The Service Manager can be contacted for further information at the numbers listed below.

  - SPARE PARTS

For our clients who have their own maintenance staff, spare parts can be ordered through our AFTER SALES SERVICE DIVISION or directly through our MANUFACTURING DIVISION at the numbers listed below.

  - WHEN ORDERING PLEASE STATE:

The Crane or Hoist W/O number.

A description of the part and part number which you can obtain from this parts list.  We recommend that you have your Cranes and Hoists inspected at least once a year by our Service Division, even if you do have your own maintenance staff.

HEAD OFFICE		(011) 873-9800 tel

HEAD OFFICE		(011) 873-9807 fax

SERVICE DIVISION 	(011) 822-2463 tel

SERVICE DIVISION	(011) 822-2469 fax

- LUBRICATION INTERVALS

| LUBRICATION INTERVALS | CLASS 1M DUTY | CLASS 2M DUTY | CLASS 3M DUTY |
| --- | --- | --- | --- |
|  | 3 MONTHS | 60 MONTHS | 6 WEEKS | 30 MONTHS | 1 MONTH | 20 MONTHS |
| Grease rope guide and rope drum Check oil level in all gearboxes and refill as necessary Change oil in hoist gearbox Change grease in travel gearboxes Grease plummer blocks Grease open reduction | X X X X | X X | X X X X | X X | X X X X | X X |

6.	LUBRICATION SPECIFICATIONS

| APPLICATION | SPECIFICATION | PETROLMARK | BP | SHELL | MOBIL |
| --- | --- | --- | --- | --- | --- |
| Hoist unit | Regular gear oil Grade SAE | Gear oil EP 90 GL 5 | BP hypogear GL 5 EP 90 | Shell spirex MB SAE 90 | Mobilube HD75W-90 |
| Drive gearboxes | Lithium soap Grease N°. 3 | Energrease FG 00 EP | Energrease FG 00 EP | Shell grease S 3655 | Mobilux EP 004 |
| Open gears | Molybdenised Lithium soap EP | Grone grease Special X | - | - | Mobil OGL 007 |
| Wheels | Lithium soap Grease N°. 2 | Super WB 3 EP | BP energrease LS 3 | Shell alvania R 3 | Mobilux EP 3 |
| Rope guide | Grease 904 Graphite grease | Energrease GP 2 G | Energrease GP 2 G | Barbatia Grease 2 | Mobilarma 798 |

Read this schedule in conjunction with the maintenance instructions.

GEARBOX OIL LEVEL

When filling with oil, do not fill above level plug, as this can cause damage to motor.

Approximate quantities of oil required for changes  :

Hoist unit			__________

Cross travel gearboxes	__________

Long travel gearboxes	__________

Slewing gearboxes	__________

## CRANE / HOIST SERVICE CHECK LIST

|  | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Steelwork | Check crane structure |  |  |  |  |  |  |
|  | Check cabin fixing and glass |  |  |  |  |  |  |
|  | Check service platforms and hand railing |  |  |  |  |  |  |
|  | Check condition of gantry |  |  |  |  |  |  |
|  | Check end stops / buffers |  |  |  |  |  |  |
|  | Check gantry rails |  |  |  |  |  |  |
|  | Check crab rails |  |  |  |  |  |  |
|  | Check monorail |  |  |  |  |  |  |
| Downshop supply | Check isolator / ACB / fuses |  |  |  |  |  |  |
|  | Check collector brackets |  |  |  |  |  |  |
|  | Check collectors, brushes |  |  |  |  |  |  |
|  | Check condition of downshop in general |  |  |  |  |  |  |
| Panel and connection boxes | Check fitting and doors (covers) |  |  |  |  |  |  |
|  | Check all contactors, relays and overloads |  |  |  |  |  |  |
|  | Check transformers |  |  |  |  |  |  |
|  | Check fuse carriers, fuses and ACB’s |  |  |  |  |  |  |
|  | Check wiring (tight / loose wires) |  |  |  |  |  |  |
|  | Check hoist, cross and long travel rectifiers |  |  |  |  |  |  |
|  | Check cable glands and earth connections |  |  |  |  |  |  |
| Pendant & pushbutton / controllers | Check enclosures |  |  |  |  |  |  |
|  | Check buttons, controllers and labels |  |  |  |  |  |  |
|  | Check pendant cable |  |  |  |  |  |  |
|  | Check pushbutton |  |  |  |  |  |  |
|  | Check cable loop and pushbutton box |  |  |  |  |  |  |
|  | Check key & selector switches (if applicable) |  |  |  |  |  |  |
| Lights and hooter (where applicable) | Check all lights fittings and globes |  |  |  |  |  |  |
|  | Check light switches and transformers |  |  |  |  |  |  |
|  | Check hooter and foot switch |  |  |  |  |  |  |
| Hoist | Check connections, terminals and cables |  |  |  |  |  |  |
|  | Check magnets and connections |  |  |  |  |  |  |
|  | Check the limit switch operating rod |  |  |  |  |  |  |
|  | Check terminals and connections |  |  |  |  |  |  |
|  | Check operation of limit switch up and down |  |  |  |  |  |  |
|  | Check ultimate limit switch (if applicable) |  |  |  |  |  |  |
|  | Check rope guide |  |  |  |  |  |  |
|  | Check rope and securing device |  |  |  |  |  |  |
|  | Check drum and rope guide nut (see note) |  |  |  |  |  |  |
|  | Check and adjust brakes |  |  |  |  |  |  |
|  | Report on condition of linings |  |  |  |  |  |  |
|  | Check for oil leaks & level of oil in gearbox |  |  |  |  |  |  |
|  | Replace oil in gearbox |  |  |  |  |  |  |
|  | (see lubrication instructions) |  |  |  |  |  |  |

NOTE  :  Please check “Lubrication Instructions” – intervals of oil and grease changes before greasing rope and

rope guide nut.  Remove impurities from these parts prior to lubrication.

| Date : ____________________ | Checked by : | Signature : |
| --- | --- | --- |

## CRANE / HOIST SERVICE CHECK LIST (continued)

|  | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Hoist | Check oil breathing plugs |  |  |  |  |  |  |
|  | Check tight fit of all supporting screws / bolts |  |  |  |  |  |  |
|  | Check load hooks for cracks cold deformation |  |  |  |  |  |  |
|  | Check condition of safety catch |  |  |  |  |  |  |
|  | Check sheaves |  |  |  |  |  |  |
| Cross travel (crab) | Check crab travel gears |  |  |  |  |  |  |
|  | Check tight fit of all supporting screws / bolts |  |  |  |  |  |  |
|  | Check and adjust brake |  |  |  |  |  |  |
|  | Check connections, terminals and cables |  |  |  |  |  |  |
|  | Check smooth running of motor and gearbox |  |  |  |  |  |  |
|  | Check cross travel limit switch (if applicable) |  |  |  |  |  |  |
|  | Replace grease in gearbox |  |  |  |  |  |  |
|  | (see lubrication instructions) |  |  |  |  |  |  |
| Long travel | Check and grease pinions and gears |  |  |  |  |  |  |
|  | Check wheels |  |  |  |  |  |  |
|  | Check tight fit of all supporting screws / bolts |  |  |  |  |  |  |
|  | Check oil breathing plugs |  |  |  |  |  |  |
|  | Check and adjust brake |  |  |  |  |  |  |
|  | Check connections, terminals and cables |  |  |  |  |  |  |
|  | Check smooth running of motor and gearbox |  |  |  |  |  |  |
|  | Check long travel limit switch (if applicable) |  |  |  |  |  |  |
|  | Replace grease in gearbox |  |  |  |  |  |  |
|  | (see lubrication instructions) |  |  |  |  |  |  |

NOTE  :  Please check “Lubrication Instructions” – intervals of oil and grease changes before greasing rope and

rope guide nut.  Remove impurities from these parts prior to lubrication.

| Date : ____________________ | Checked by : | Signature : |
| --- | --- | --- |

STANDARD CRANE ELECTRICAL CIRCUIT DIAGRAM

NOTE: FOR HOIST AND CRAWL UNITS LONG TRAVEL DOESN’T APPLY’

FOR NON-STANDARD CRANES SEE SPECIALLY DESIGNED DIAGRAMS.

# Text boxes

Page 1

On a STANDARD CRANE the supply & long travel switch gear are housed in one control panel placed on the end carriage and the hoist & cross travel switchgear are housed in another control panel on the back of the hoist

Page 2

Page 3

Page 4

Page 7

Page 8

Page 9

Page 5

Page 6